## Slide 1
Light-Brakers
ECEN 1400-012, Group 21
10/22/25

## Slide 2
Team Members
Rowan McCune
Electrical Engineering
Hall-Effect Sensor
Jacob Nguyen
Electrical Engineering
LED Array
Roman Tagliola
Aerospace Engineering
LCD Display
Mitchell Vallis
Electrical Engineering
Accelerometer

## Slide 3
Problem Statement
Bikes generally don’t have a brake light indicating when the cyclist is braking
Congested bike lanes can reduce the rider’s reaction time, leading to crashes

## Slide 4
Outline
Problem
Idea
Concept
Concept
Risk Mitigation
Risk Mitigation
Testing
Testing
Timeline
Bill of Materials
Summary
LED Module Outline
Display Module Outline

## Slide 5
Dynamic Brake Light Software Diagram
Hall-Effect Sensor
Controller
LCD Display
User Interface and Kinematic Computations
User Configured
Information
Data collection
Accelerometer
Controller
LED Array
Process Data
Light Output
Data collection
Data
Bluetooth

## Slide 6
LED Module: Components
Lithium Ion Battery, 850 mAh
Accelerometer
ADXL335
ESP32 Thing Plus
Super Bright Red LED (10000mcd)
Brake Light Casings

## Slide 7
LED Module: Electrical Block Diagram
3.7V 850mAh Lion Battery
17 LEDs in parallel
Power Requirements:
In Parallel, 2.0V to 2.4V
Max Current of 340mA
Up to 10000mcd per
Battery Life: ~4 hours
x17

## Slide 8
LED Module: CAD Drawings
Front
Back
17 LEDS
Two Pieces
  Each 2" x 2" x 1.45"
    Inside 1.6" x 1.6" x 2"
  Connection:
    Slots and Ridges
Accessible USB-C Port
Front has a LED Bulb Hole and a LED Leg Hole
Split Ring Pipe Clamp Attachment

## Slide 9
LED Module: Risk Mitigation
Hardware | Software
Circuit damage from vibrations | Ensure light brightness is appropriate to how quickly we are slowing down
Casing not being weather-resistant | Make sure external noise doesn't throw off acceleration measurements
Weak mount / stable attachment to the bike | Issues with connecting to Bluetooth

## Slide 10
LED Module: Testing Plan
Hardware | Software
Testing circuit resistance to vibrations and bumps with trial rides | Trial runs on the bike to fine tune brightness of LEDs
Testing casing vibrational resistance and reliability with trial rides | Refine code to reduce noise when accelerometer is mounted
Ensuring zero-tolerance casing fit | Power cycle the brake light to ensure it connects to Bluetooth every time

## Slide 11
Display Module: Components
ESP32 Thing Plus
2.2” Color LCD TFT Display
Linear 3D
Hall-Effect Sensor
TMAG5273
Lithium Ion Battery, 850 mAh

## Slide 12
Display Module: Electrical Block Diagram
3.7V 850mAh Lion Battery
Power Requirements:
Total Power: ~0.823W
Current: ~222.3mA
Battery Life: ~3 hours 49 minutes

## Slide 13
Display Module: CAD Drawings
Prongs that hold module in place
Zip-tie ports
"Zero-tolerance" weather seal
Buttons to adjust display UI
Clamp mount
with interior rubber paint
Clamshell secured by nuts and bolts
Display Module:
1.0 inch thick
(total w/o clamp and buttons)
3.6 inches tall
3.0 inches wide
Hall-Effect Sensor Housing:
1.0 inches long
2.0 inches wide
0.75 inch tall

## Slide 14
Display Module: Risk Mitigation
Hardware | Software
Original display non-functional out of the box | Intuitive and non-intrusive user interface
Proper fitment of display components inside housings | Stable Bluetooth connection
Circuit damage due to vibrations | Conversion rate and accuracy of Hall-Effect sensor
Magnetic Sensitivity | 1-axis read measurement conversion
Tachometer Sensor Calibration:

## Slide 15
Display Module: Testing Plan
Hardware | Software
Mount display module on handle-bar to test stability of mount | Use cardboard plate to test for consistent, stable Bluetooth connections
Ride bike both with the display and with an iPhone to gauge display reading accuracy | Test non-intrusive UI though trial rides
Successfully mount magnets on bike wheel | Track distance travelled with the Hall-Effect sensor and with GPS, measuring accuracy

## Slide 16
Gantt
Chart

## Slide 17
Bill of Materials
Component | Price (USD) | Supplier
SparkFun Triple Axis Accelerometer Breakout | $20 | Amazon
SparkFun Linear 3D Hall-Effect Sensor | $7 | Amazon
LED – Super Bright Red (25 Pack) | $5 | SparkFun Electronics
SparkFun Qwiic Cable Kit | $13 | SparkFun Electronics
SparkFun Capacitor Kit | $12 | SparkFun Electronics
2.2" 18-Bit Color TFT LCD with MicroSD Card Breakout – EYESPI Connector | $25 | AdaFruit Industries
2x SparkFun Thing Plus – ESP32 WROOM (Micro-B) | $25 Each $50 Total | SparkFun Electronics
Total | $132 | 

## Slide 18
Summary
Identified a problem in the biking community
Explained our solution to this problem
Reviewed the technical execution of our solution and how each component is implemented
Explained risks, testing plan and project management

## Slide 19
Questions?